### Transport model
We consider landfill as a set of stream tubes. Here a stochastic particle tracking approach is used. Each water particle entering one of the stream tubes receives its random travel time (following a log-normal distribution) depending on the properties of the tube. Hence the out flow can be described by:
Q_"out"(t)=int csup {t} csub {0} {Q_"in"(%tau) cdot f(t-%tau) {d%tau}},	(1)
where f(t-%tau) is a log-normal PDF.
Parameters of a log-normal PDF for a single input pulse vary depending on the actual moisture content in a column. Fig. 1 illustrates relationships between the effective saturation of a 1D column and parameters μ (a) and σ (b) of a log-normal PDF that approximated an observed breakthrough curve most accurately. These results are illustrative and must be precomputed for a particular hydraulic properties of a given waste.
a) b)
Fig. 1. Dependency of parameters of log-normal distribution μ (a) and σ (b) on effective saturation.
Fig. 3 shows two possible outputs for (1) in case of μ and σ variable with moisture content (blue line) and constant parameters (green line) for precipitation data shown in Fig. 2.

Fig.2.Input precipitation data.

Fig. 3.Test outflux from a landfill for contant parameters of log-normal distribution (green line) and variable parameters (blue line)