# Approximating Richard's equation: 1D case
## Theory
We consider 1-dimensional column of soil partly saturated with water. At different times some amounts of water are applied at the top of column. We are interested in the behavior of the described system in terms of output flux at the bottom of column.
The aforementioned system can be described using Richards equation. Richards equation may be solved numerically providing accurate enough description of hydrodynamical behavior inside the column. However numerical solution of Richards equation requires a lot of computational resources. In order to get fast solution we are trying to approximate the result of Richards equation.
The system is constantly responding to input fluxes applied. The response for a single input pulse at a given time can be approximated using log-normal distribution. Hence the out flow can be calculated as:
Q_"out"(t)=int csup {t} csub {0} {Q_"in"(%tau) cdot func P_ln(t-%tau) {d%tau}},	(1)

where func P_ln(t-%tau) is a log-normal PDF:
func P_ln(t) = 1 over {t cdot sqrt{2 cdot %pi cdot %sigma^2}} cdot func e^{- (func ln{t} - %mu)^2 over {2 cdot %sigma^2}} .	(2)

Parameters μ and σ of a log-normal PDF for a single input pulse vary depending on many parameters of the Richards equation.
### Determining log-normal parameters
A finite difference method is used to numerically solve Richards equation assuming Dirac delta function as a top boundary condition, i.e. single input pulse at initial time and no influx afterwards. The system was in equilibrium at the moment of injection. The dynamics of flux at the bottom of the column is computed for different sets of input parameters and later analyzed.
Log-normal distribution can be characterized by two parameters, commonly denoted as μ and σ. Where μ is a location parameter and σ – scale parameter. These parameters may be obtained having distribution of out flux at the bottom of column at different times:
%mu = ln(E) - 1 over 2 cdot ln(1 + Var over {E ^ 2});	(3)

%sigma^2 = ln(1 + Var over {E^2}),	(4)

where E – expected value, Var – variance, which can be easily calculated using statistical theory.
Figure 1 compares shapes of output flux curve as response to instantaneous injection versus log-normal curve with picked μ and σ for two different sets of input parameters.

a)

b)
Fig. 1. Comparison of output flux as a result of numerical solution of Richards equation vs. its approximation using log-normal distribution.
Our intention here is to characterize flux properties to a minimized number of parameters like hydraulic conductivity, average effective saturation in the column(van Genuchten) etc. which can be later translated to parameters of log-normal distribution.
Figures 3 and 3 show dependencies of log-normal parameters on hydraulic conductivity.

Fig. 2. Relationship between hydraulic conductivity and parameters μ, σ.

Fig. 3. Relationship between hydraulic conductivity and parameters μ, σ.
As can be seen from figures 3 and 3 the value of σ remains constant with changes in hydraulic conductivity, while the shape of μ-curve resembles shifted negative logarithmic curve. The latter statement makes sense since the breakthrough time is inversely proportional to hydraulic velocity and hence the mean breakthrough time will be also inversely proportional to conductivity:

T_mean = func e^{v} over K_sat,	(5)

where: T_mean is the expected breakthrough time, K_sat – saturated conductivity, func e^{v} – constant coefficient of proportionality. On the other hand:
T_mean = func e^{%mu + %sigma^2 over 2}.	(6)

A dependency of μ as a function of K_sat may be derived based on (5) and (6):
%mu = -ln(K_sat) + %omega .	(7)

Here %omega = v + %sigma^2 over 2 is the aforementioned shift which depends on the properties of column and initial conditions. Knowing this shift one can easily estimate outflux at the bottom of the column for different values of hydraulic conductivity.
Figures 4 and 5 show dependencies of log-normal parameters on the average effective saturation in the column.

Fig. 4. Relationship between average effective saturation and parameters μ, σ.

Fig. 5. Relationship between average effective saturation and parameters μ, σ.

### Modelling flow
Knowing how the changes in hydraulic properties of the system affect parameters of log-normal approximation of outflow one can model the outflow.
Preparatory calculations:
1. First Richards equation has to be solved numerically for different values of average effective saturation and desired water retention parameters (e.g. %theta_r, %theta_s, %alpha, %lambda ). The latter are assumed to remain constant.
2. Determining log-normal parameters for each numerical solution using (3), (4). Storing values of average effective saturation and corresponding values of log-normal parameters to a table.
Actual calculations:
1. Lookup for a given value of effective saturation and corresponding %mu_0 and %sigma in previously compiled table, interpolate if necessary.
2. Adjust value of %mu_0 . to a given value of hydraulic conductivity. Here expression (7) is used, where %omega = %mu_0 . Hence :
%mu = -ln(K_sat over K_ref) + %mu_0 = -ln(K_sat) + ln(K_ref) + %mu_0,	(8)

where K_ref is the reference saturated conductivity, i.e. conductivity used during preparatory calculations.
Numerically integrate (1) to estimate flux at the bottom of the column as response of the system to water supply at the top.
Figure 6 shows possible output for (1) in comparison with the actual input used.

Fig. 6: Sample output of output flux estimate vs. input flux

Fig. 7: Comparison of output flux modeled using FDM solution of Richards equation (red) vs. using log-normal transfer function

Fig. 8: Sample outputs assuming variable (blue) and constant (green) effective saturation in the column

### Some issues