# Transport model
## Theory
We consider landfill as a set of stream tubes. Here a stochastic particle tracking approach is used. Each water particle entering one of the stream tubes receives its random travel time (following a log-normal distribution) depending on the properties of the tube. Hence the out flow can be described by:
Q_"out"(t)=int csup {t} csub {0} {Q_"in"(%tau) cdot func P_ln(t-%tau) {d%tau}},	(1)
where func P_ln(t-%tau) is a log-normal PDF:
func P_ln(t) = 1 over {t cdot sqrt{2 cdot %pi cdot %sigma^2}} cdot func e^{- (func ln{t} - %mu)^2 over {2 cdot %sigma^2}} .	(2)
Parameters of a log-normal PDF for a single input pulse vary depending on the actual moisture content in a column. Fig. 1 illustrates relationships between the effective saturation of a 1D column and parameters μ (a) and σ (b) of a log-normal PDF that approximated an observed breakthrough curve most accurately. These results are illustrative and must be precomputed for a particular hydraulic properties of a given waste.
a) b)
Fig. 1. Dependency of parameters of log-normal distribution μ (a) and σ (b) on effective saturation.
Fig. 3 shows two possible outputs for (1) in case of μ and σ variable with moisture content (blue line) and constant parameters (green line) for precipitation data shown in Fig. 2.

Fig.2.Input precipitation data.

Fig. 3.Test outflux from a landfill for contant parameters of log-normal distribution (green line) and variable parameters (blue line)
## Matlab code
This section briefly describes the model code.
### Versions implemented
#### 1D version
3 different 1D versions of the model are implemented:
- simple 1D model;
- 2 domain 1D model;
- 2 domain 1D model with exchange between pathways.
All these implementations consider a vertical column of cells conducting liquids. For 2 domain flow 2 parallel columns are assumed. All incoming rain water is distributed between them.
#### 2D version
This version of a model considers a landfill as a 2D array of columns of different heights.
#### 3D version
This version of a model considers a landfill as a 3D array of cells. Here vertical sequence of cells composes a column as in 2D version.
### General structure of the main script
Despite the versions of the model are different they all have common structure. The main function consists of the following parts:
- Preparing data for simulation. This includes:
  - definition of a column/landfill geometry;
  - definition of time parameters of simulation (in case the precipitation data are read from an input file, the time parameters are also read/initialized from this file);
  - initializing log-normal parameters computing object;
  - definition of hydraulic properties of a conducting medium;
  - definition of initial moisture content, bio-geochemical properties of the waste;
  - reading/generating precipitation data.
- Main simulation loop. Here the function called transport_lognormal() is called for every time-step. In general, it applies expression (1) on every time-step and for each cell. If two or more cells are located vertically, then the out-flow from the upper cell is considered as in-flow into the lower one. The outflow during the time interval [t_n,t_n+%DELTA t] is calculated as:
M= C_0 cdot int csub{t_n} csup{t_n + %DELTA t} {func P_ln(t) cdot dt}= C_0 cdot (func CDF_ln(t_n + %DELTA t)-func CDF_ln(t_n)),
where func CDF_ln(t) − is the log-normal cumulative density function. Using of a CDF allows obtaining better mass balance especially when the time step is too big compare to the response time of the system.
Plotting/analysis of results.
### Controlling flow
#### Log-normal parameters definer
Log-normal parameters definer is used to define position (μ) and shape (σ) parameters of a log-normal PDF (2).
These parameters vary with changes in hydraulic conductivity and moisture content. Fig. 4 shows two more examples of such dependency in addition to fig. 1.

Fig. 4. Dependency of parameters of log-normal distribution (from left to right μ and σ) on effective saturation for a 1 m high column.
The aforementioned log-normal PDF defines probability of breakthrough for a unit volume of water applied at the inlet of a cell. These dependencies are precomputed and stored as a table. In order to determine what values of μ and σ correspond to a given combination of hydraulic conductivity and (mention about μ as a function of hydraulic conductivity) moisture content, a simple interpolation will be used during the runtime.
Log-normal parameters definer is used every time before calling log-normal probability function that computes amount of water that crossed the bottom of control cell.
Despite the fact that dependencies of μ and σ of moisture content are precomputed for a given hydraulic conductivity, DESCRIBE DEPENDENCY OF MU OF CONDUCTIVITY
#### Exchange rate (1 dimension 2 domains with exchange)
Exchange between domains can be set in 1-dimensional model with exchange between matrix and channel domain (main_1d_2domain_exchange_flow.m). The value for exchange specifies the rate of liquid entering a matrix domain cell that leaves immediately to the channel domain. This can be a single percentage value as well as a function of depth:
exchange_rate = 0.2 * (1 - 1 / max(z)^(1/2) * z.^(1/2));
#### Matrix/Channel volume ratio (1 dimension 2 domains versions only)
1-dimensional models assume a column of height H with a cross-section of 1m ´ 1m. This column is divided into two domains for 2-domain models. In such cases the percentage of channel domain in the total volume is specified by the chan_width variable.
#### Distribution of hydraulic conductivities among columns/pathways (2D and 3D models)
The way, hydraulic conductivities are distributed among pathways may be specified in a function generate_conductivities(spatial_params). Conductivity is assumed to be constant for each column, but differ from one column to another. The function gets geometrical properties spatial_params of the landfill as an input parameter.
# Solute Transport
## Theory
Convection-diffusion equation (CDE) describes behavior of solute concentration:
{partial C(z,t)} over {partial t} = D cdot {{partial^2 C(z,t)} over {{partial z}^2}} - V cdot {{partial C(z,t)} over {partial z}};
Hereafter we assume constant clean water influx and initial concentration of C_0 solute throughout the column. Hence the initial and boundary conditions are:
C(z, 0) = ~~~ stack{C_{0}, 0 < z leslant L, # 0, otherwise;} C(0, t) = 0;

The analytical solution of this system is:
C(z, t) = - {{C_{0}} over {2}} cdot erf({-z + V cdot t} over {2 cdot sqrt(D cdot t)}) + {{C_{0}} over {2}} cdot erf({-z + L + V cdot t} over {2 cdot sqrt(D cdot t)});
PDF's of escape times for solute particles leaving column of height L downwards can be calculated as:
P(t)=-{1 over {C_0 cdot L}} cdot {partial over {partial t}} cdot int csub {-infinity} csup {L} {C(z,t)dt} = {V over 2} cdot erf({L-V cdot t} over {2 cdot sqrt{D cdot t}}) + {V over 2} cdot erf({V cdot t} over {2 cdot sqrt{D cdot t}}) +{}	+ {sqrt D over {2 cdot sqrt{%pi cdot t}} cdot exp(-{(V cdot t)^2 over {4 cdot t cdot D}}) - sqrt D over {2 sqrt{%pi cdot t}} cdot exp(-{(L-V cdot t)^2 over {4 cdot t cdot D}})};

Fig. 4. PDF of particle escape times for different parameters