# Approximating Richard's equation: 1D case
## Theory
We consider 1-dimensional column of soil partly saturated with water. At different times some amounts of water are applied at the top of column. We are interested in the behavior of the described system in terms of output flux at the bottom of column.
The aforementioned system can be described using Richards equation. Richards equation may be solved numerically providing accurate enough description of hydrodynamical behavior inside the column. However numerical solution of Richards equation requires a lot of computational resources. In order to get fast solution we are trying to approximate the result of Richards equation.
The system is constantly responding to input fluxes applied. The response for a single input pulse at a given time can be approximated using log-normal distribution. Hence the out flow can be calculated as:
Q_"out"(t)=int csup {t} csub {0} {Q_"in"(%tau) cdot func P_ln(t-%tau) {d%tau}},	(1)

where func P_ln(t-%tau) is a log-normal PDF:
func P_ln(t) = 1 over {t cdot sqrt{2 cdot %pi cdot %sigma^2}} cdot func e^{- (func ln{t} - %mu)^2 over {2 cdot %sigma^2}} .	(2)

Parameters μ and σ of a log-normal PDF for a single input pulse vary depending on many parameters of the Richards equation.
### Determining log-normal parameters
A finite difference method is used to numerically solve Richards equation assuming Dirac delta function as a top boundary condition, i.e. single input pulse at initial time and no influx afterwards. The system was in equilibrium at the moment of injection. The dynamics of flux at the bottom of the column is computed for different sets of input parameters and later analyzed.
Log-normal distribution can be characterized by two parameters, commonly denoted as μ and σ. Where μ is a location parameter and σ – scale parameter. These parameters may be obtained having distribution of out flux at the bottom of column at different times:
%mu = ln(E) - 1 over 2 cdot ln(1 + Var over {E ^ 2});	(3)

%sigma^2 = ln(1 + Var over {E^2}),	(4)

where E – expected value, Var – variance, which can be easily calculated using statistical theory.
Figure 1 compares shapes of output flux curve as response to instantaneous injection versus log-normal curve with picked μ and σ for two different sets of input parameters.

Our intention here is to characterize flux properties to a minimized number of parameters like hydraulic conductivity, average effective saturation in the column(van Genuchten) etc. which can be later translated to parameters of log-normal distribution.
Figures 2 and 3 show dependencies of log-normal parameters on hydraulic conductivity.

a)

b)
Fig. 1. Comparison of output flux as a result of numerical solution of Richards equation vs. its approximation using log-normal distribution.
Fig. 2. Relationship between hydraulic conductivity and parameters μ, σ.

Fig. 3. Relationship between hydraulic conductivity and parameters μ, σ.
As can be seen from figures 2 and 3 the value of σ remains constant with changes in hydraulic conductivity, while the shape of μ-curve resembles shifted negative logarithmic curve. The latter statement makes sense since the breakthrough time is inversely proportional to hydraulic velocity and hence the mean breakthrough time will be also inversely proportional to conductivity:

T_mean = func e^{v} over K_sat,	(5)

where: T_mean is the expected breakthrough time, K_sat – saturated conductivity, func e^{v} – constant coefficient of proportionality. On the other hand:
T_mean = func e^{%mu + %sigma^2 over 2}.	(6)

A dependency of μ as a function of K_sat may be derived based on (5) and (6):
%mu = -ln(K_sat) + %omega .	(7)

Here %omega = v + %sigma^2 over 2 is the aforementioned shift which depends on the properties of column and initial conditions. Knowing this shift one can easily estimate outflux at the bottom of the column for different values of hydraulic conductivity.
Figures 4and 5 show dependencies of log-normal parameters on the average effective saturation in the column.

Fig. 4: Relationship between average effective saturation and parameters μ, σ.

Fig. 5: Relationship between average effective saturation and parameters μ, σ.
### Modelling flow
Knowing how the changes in hydraulic properties of the system affect parameters of log-normal approximation of outflow one can model the outflow.
Preparatory calculations:
1. First Richards equation has to be solved numerically for different values of average effective saturation and desired water retention parameters (e.g. %theta_r, %theta_s, %alpha, %lambda ). The latter are assumed to remain constant.
2. Determining log-normal parameters for each numerical solution using (3), (4). Storing values of average effective saturation and corresponding values of log-normal parameters to a table.
Actual calculations:
1. Lookup for a given value of effective saturation and corresponding %mu_0 and %sigma in previously compiled table, interpolate if necessary.
2. Adjust value of %mu_0 . to a given value of hydraulic conductivity. Here expression (7) is used, where %omega = %mu_0 . Hence :
%mu = -ln(K_sat over K_ref) + %mu_0 = -ln(K_sat) + ln(K_ref) + %mu_0,	(8)

where K_ref is the reference saturated conductivity, i.e. conductivity used during preparatory calculations.
Numerically integrate (1) to estimate flux at the bottom of the column as response of the system to water supply at the top.
Figure 6 shows possible output for (1) in comparison with the actual input used.

Fig. 6: Sample output of output flux estimate vs. input flux
Figure 7 compares flux rates at the bottom of the column modelled using finite difference solution of Richards equation (red line) vs. the one modelled using log-normal transport function.

Fig. 7: Comparison of output flux modeled using FDM solution of Richards equation (red) vs. using log-normal transfer function
As can be seen from figure 7, the approximation of flux using log-normal transfer function is rather accurate. However hydrodynamical properties and hence the breakthrough time of the system change constantly together with flow. This is because the real hydraulic conductivity depends on current effective saturation of the column. The relationships are presented in figures 4 and 5 may be used to constantly update log-normal parameters of the system depending on the actual moisture content. The latter can be easily calculated based on the mass balance. Figure 8 shows how variable moisture content can influence the output of transfer function.

Fig. 8: Sample outputs assuming variable (blue) and constant (green) effective saturation in the column

## Some issues

### Limiting influx
Using log-normal transfer function doesn't take into account the physics of the system. Thus all the input amount of water is distributed at the output over time according to a log-normal distribution. While the real system can only digest the amount of water that:
can pass through the top surface in the given time interval;
and
can fit into the available free pore space.
### Increasing column height vs. sequence of cells
Following figures 9 and 10 illustrate how parameters of log-normal distribution change together with increasing column height. During this experiment the position of water table was assumed at the bottom of column.

Fig. 9: Relationship between column height and parameters μ, σ, assuming water table at the bottom of landfill

Fig. 10: Relationship between column height and parameters μ, σ, assuming water table at the bottom of landfill
As can be seen from figures 9 and 10 changes in parameter μ resemble logarithmic curve (see fig. 11) while σ steeply decreases for lengths shorter than 10 m and after 10 m stays almost constant around value 0.607-0.608.

Fig. 11: Variations of parameter μ with column length and their logarithmic approximates.
At the same time analysis of behavior of sequence of 1 meter high columns was carried out. Here all the flux at the outlet of the top column on every time step was passed to the input of a column below and collected at the bottom of the last column. Considering assumption of log-normal distribution of outflux for each cell, the output is also log-normally distributed. Its distribution corresponds to distribution of a sum of random variables, each following log-normal distribution corresponding to a particular cell (derived empirically – reference?). Based on the fact that expected value (EV) and variance of sum of log-normal variables equals to sum of EVs and sum of variances respectively (refer), corresponding expressions for parameters μ and σ may be analytically derived.

Consider sequence of n columns, each 1 meter high. With the water table level at the bottom of the lowest column i.e. -n meters. The algorithm is as follows:
1. Compute average effective saturation for each column using van Genuchten retention curve.
2. Find values of μ and σ corresponding to effective saturation in each column.
3. Compute EV and variance of outflow distribution for each cell using previously obtained μ and σ.
4. Sum up EVs and variances. This will result in EV and variance of outflux distribution for a column of a hight n.
5. Having EV and variance for the entire column, values of μ and σ may be computed.
The black curves on figures 12 and 13 illustrate the results of application such an algorithm. The red lines denote values of parameters obtained from application of log-normal transfer function for a sequence if cells. As one can see, these two types of curves demonstrate very good agreement. However they are far enough from the results obtained from numerical solutions of Richards equation.

Fig. 12: Comparison of changes of μ and σ with column length.

Fig. 13: Comparison of changes of μ and σ with column length.
Based on the above we may see that getting using a sequence of log-normal transport functions doesn't provide us with a good approximate of the Richards solution. This is mainly due to a large discrepancy of values for σ, which tends to much narrower output signal taking place earlier as compare to Richards solution.
It may be possible to solve Richards equation for a desired cell height and use this.
### Possible optimization / implications
Expected value and variance of a sum of log-normal random variables equals sum of expected values and variances respectively. This means that the model may be optimized by modeling only one random variable with proper parameters to match final breakthrough.