# Approximating Richard's equation: 1D case
## Theory
We consider landfill as a set of stream tubes. Here a stochastic particle tracking approach is used. Each water particle entering one of the stream tubes receives its random travel time (following a log-normal distribution) depending on the properties of the tube. Hence the out flow can be described by:
Q_"out"(t)=int csup {t} csub {0} {Q_"in"(%tau) cdot func P_ln(t-%tau) {d%tau}},	(1)
where func P_ln(t-%tau) is a log-normal PDF:
func P_ln(t) = 1 over {t cdot sqrt{2 cdot %pi cdot %sigma^2}} cdot func e^{- (func ln{t} - %mu)^2 over {2 cdot %sigma^2}} .	(2)
Parameters of a log-normal PDF for a single input pulse vary depending on the actual moisture content in a column. Fig. 1 illustrates relationships between the effective saturation of a 1D column and parameters μ (a) and σ (b) of a log-normal PDF that approximated an observed breakthrough curve most accurately. These results are illustrative and must be precomputed for a particular hydraulic properties of a given waste.
a) b)
Fig. 1. Dependency of parameters of log-normal distribution μ (a) and σ (b) on effective saturation.
Fig. 3 shows two possible outputs for (1) in case of μ and σ variable with moisture content (blue line) and constant parameters (green line) for precipitation data shown in Fig. 2.

Fig.2.Input precipitation data.

Fig. 3.Test outflux from a landfill for contant parameters of log-normal distribution (green line) and variable parameters (blue line)
## Matlab code
This section briefly describes the model code.
### Versions implemented
#### 1D version
3 different 1D versions of the model are implemented:
- simple 1D model;
- 2 domain 1D model;
- 2 domain 1D model with exchange between pathways.
All these implementations consider a vertical column of cells conducting liquids. For 2 domain flow 2 parallel columns are assumed. All incoming rain water is distributed between them.
#### 2D version
This version of a model considers a landfill as a 2D array of columns of different heights.
#### 3D version
This version of a model considers a landfill as a 3D array of cells. Here vertical sequence of cells composes a column as in 2D version.
### General structure of the main script
Despite the versions of the model are different they all have common structure. The main function consists of the following parts:
- Preparing data for simulation. This includes:
  - definition of a column/landfill geometry;
  - definition of time parameters of simulation (in case the precipitation data are read from an input file, the time parameters are also read/initialized from this file);
  - initializing log-normal parameters computing object;
  - definition of hydraulic properties of a conducting medium;
  - definition of initial moisture content, bio-geochemical properties of the waste;
  - reading/generating precipitation data.
- Main simulation loop. Here the function called transport_lognormal() is called for every time-step. In general, it applies expression (1) on every time-step and for each cell. If two or more cells are located vertically, then the out-flow from the upper cell is considered as in-flow into the lower one. The outflow during the time interval [t_n,t_n+%DELTA t] is calculated as:
M= C_0 cdot int csub{t_n} csup{t_n + %DELTA t} {func P_ln(t) cdot dt}= C_0 cdot (func CDF_ln(t_n + %DELTA t)-func CDF_ln(t_n)),
where func CDF_ln(t) − is the log-normal cumulative density function. Using of a CDF allows obtaining better mass balance especially when the time step is too big compare to the response time of the system.
Plotting/analysis of results.
### Controlling flow
#### Log-normal parameters definer
Log-normal parameters definer is used to define position (μ) and shape (σ) parameters of a log-normal PDF (2).
These parameters vary with changes in hydraulic conductivity and moisture content. Fig. 4 shows two more examples of such dependency in addition to fig. 1.

Fig. 4. Dependency of parameters of log-normal distribution (from left to right μ and σ) on effective saturation for a 1 m high column.
The aforementioned log-normal PDF defines probability of breakthrough for a unit volume of water applied at the inlet of a cell. These dependencies are precomputed and stored as a table. In order to determine what values of μ and σ correspond to a given combination of hydraulic conductivity and (mention about μ as a function of hydraulic conductivity) moisture content, a simple interpolation will be used during the runtime.
Log-normal parameters definer is used every time before calling log-normal probability function that computes amount of water that crossed the bottom of control cell.
Despite the fact that dependencies of μ and σ of moisture content are precomputed for a given hydraulic conductivity, DESCRIBE DEPENDENCY OF MU OF CONDUCTIVITY
#### Exchange rate (1 dimension 2 domains with exchange)
Exchange between domains can be set in 1-dimensional model with exchange between matrix and channel domain (main_1d_2domain_exchange_flow.m). The value for exchange specifies the rate of liquid entering a matrix domain cell that leaves immediately to the channel domain. This can be a single percentage value as well as a function of depth:
exchange_rate = 0.2 * (1 - 1 / max(z)^(1/2) * z.^(1/2));
#### Matrix/Channel volume ratio (1 dimension 2 domains versions only)
1-dimensional models assume a column of height H with a cross-section of 1m ´ 1m. This column is divided into two domains for 2-domain models. In such cases the percentage of channel domain in the total volume is specified by the chan_width variable.
#### Distribution of hydraulic conductivities among columns/pathways (2D and 3D models)
The way, hydraulic conductivities are distributed among pathways may be specified in a function generate_conductivities(spatial_params). Conductivity is assumed to be constant for each column, but differ from one column to another. The function gets geometrical properties spatial_params of the landfill as an input parameter.
# Solute Transport
## Theory
Convection-diffusion equation (CDE) describes behavior of solute concentration:
{partial C(z,t)} over {partial t} = D cdot {{partial^2 C(z,t)} over {{partial z}^2}} - V cdot {{partial C(z,t)} over {partial z}};	(3)
In the first case we assume constant clean water influx and initial concentration of C_0 solute throughout the column. Hence the initial and boundary conditions are:
C(z, 0) = ~~~ stack{C_{0}, 0 < z leslant L, # 0, otherwise;} C(0, t) = 0;	(4)

The analytical solution of system (3), (4) is:
C(z, t) = - {{C_{0}} over {2}} cdot erf({-z + V cdot t} over {2 cdot sqrt(D cdot t)}) + {{C_{0}} over {2}} cdot erf({-z + L + V cdot t} over {2 cdot sqrt(D cdot t)});
PDF's of escape times for solute particles leaving column of height L downwards can be calculated as:
P(t)=-{1 over {C_0 cdot L}} cdot {partial over {partial t}} cdot int csub {-infinity} csup {L} {C(z,t)dz} = {V over 2} cdot erf({L-V cdot t} over {2 cdot sqrt{D cdot t}}) + {V over 2} cdot erf({V cdot t} over {2 cdot sqrt{D cdot t}}) +{}	+ {sqrt D over {2 cdot sqrt{%pi cdot t}} cdot exp(-{(V cdot t)^2 over {4 cdot t cdot D}}) - sqrt D over {2 sqrt{%pi cdot t}} cdot exp(-{(L-V cdot t)^2 over {4 cdot t cdot D}})};	(5)

Fig. 4. PDF of particle escape times for different parameters
The second interesting case is a single input pulse of solute concentration C_0 at time t=0 (Dirac delta function) to the initially clean system:
C(z, 0) = 0, C(0, t) = C_0 cdot %delta(t).	(6)
The system (3), (6) has following analytical solution:
C(z, t) = {-{C_{0} cdot {z over {2 cdot sqrt{%pi cdot D cdot t^3}}}} cdot exp(-(z - V cdot t)^2 over {4 cdot D cdot t})} ;
By integrating this solution as in (5) we obtain the following probability distribution of escape times:
P(t)=1 over C_0 cdot {(L cdot V cdot t - 2 cdot D cdot t + L^2) over {4 cdot sqrt{%pi cdot d cdot t^5}}} cdot func exp(- (L - V cdot t)^ 2 over {4 cdot D cdot t}).	(7)
Fig. 5 shows plots for several combinations of parameters.

Fig. 5. PDF of particle escape times for different parameters
### Scaling to variable flow
In order to account for variable flow we consider two cases:
- Matrix domain. We assume here that solute transport is mostly dominated by diffusion (hence D >> V ). In this case we neglect any fluctuations in V.
- Channel domain. In this case we make an opposite assumption that the flow is the dominant process in solute transport ( D << V ). Here we neglect diffusion, or to be more precise scale it together with changes in flux rate.
Formulas (5) and (7) have been derived for constant flow ( V(t)=func const=V_0 ). Hence we can rewrite them as functions of cumulative flux instead of time:
P(t) equiv P_S(S(t)) ,	(8)
where P_S(S(t)) - is a PDF of escape times as a function of relative cumulative flux calculated as follows:
S(t) = 1 over V_0 cdot {int csub {0} csup {t} V(t) cdot d%tau } ,	(9)
with V_0 = V(0) . In case of constant flux S(t) = t hence P_S(t) equiv P(t) . While for variable flux the PDF will be as follows:
P(t) = {V(t)} over V_0 cdot P(1 over V_0 cdot int csub {0} csup {t} V(%tau) cdot d%tau ) .	(10)
Factor {V(t)} / V_0 is introduced in order to keep the mass balance correct. This is due to the fact that we squeeze/stretch the time axis, but the amount of solute leaving system should be the same as for constant flow. Therefore for e.g. faster flow and hence squeezed (less) time the solute leaving system per unit time should be higher, while still the same for the total amount of flux during this time.